## Slide 1: CRANES & RIGGING
Presented by:
Kurt Rayburg, CSP, CPEA
Safety Manager - CURI

## Slide 2: Terminology
Crane – a machine for lifting and lowering a load and moving it horizontally, with the hoisting mechanism. Cranes are driven manually or by power.
Derrick – an apparatus consisting of a mast held at the head by guys or braces, with or without a boom, for use with a hoisting mechanism and operating ropes.

## Slide 3: Terminology
Certified Operator – a person who has successfully completed a training curriculum from an accredited crane operator testing program. (Crane Institute/NCCCO)
Qualified Person – a person who, by possession of a recognized degree, certificate or professional standing, or by extensive training, knowledge and experience, successfully demonstrates the ability to solve or resolve issues related to a subject matter.
Competent Person – a person who is capable of identifying existing and predictable hazards and has the authority to take corrective action.

## Slide 4: Types of Cranes
Crawler
Gantry
Tower
Mobile
Overhead
Jib

## Slide 5: CURI Cranes

## Slide 6: Crane Compass

## Slide 7: Training
OSHA has a deadline for crane operators certification to November 10th, 2018. (Construction Standard)
Testing agencies must be accredited by a nationally recognized accrediting agency based on criteria for;
    - Written and practical exams
    - Testing materials / grading
    - Facilities and equipment
Industrial 1910.179(b)(8)
- Only designated personnel shall be permitted to operate a crane.

## Slide 8: Crane Inspections
Each Shift - Competent person must inspect prior to each shift (use).
Monthly – Competent person must document monthly inspection and retain for 3 months.
Annual - Qualified person must inspect, disassemble and functionally test. Retain document for 1 year
*Certification training includes inspection techniques.

## Slide 9: Operational Inspection
Move crane several feet in each direction
Unusual noises and jerky movements
Control station and switches work correctly
Lower hoist block to make sure at least 2 turns of rope remain on drum
Hook has a safety latch and it’s not stretched.

## Slide 10: Visual Inspection
Look for crane tags
Look for physical damage
Check hoist chain and wire rope
Make sure wire rope is seated in drum and sheave grooves
Look for disconnect switch.

## Slide 12: Rigging – What We Need To Know
Employers must ensure:
1) inspection prior to use
2) permanent markings are affixed showing safe working load
3) not to be loaded in excess of working load
4) not to be used without affixed markings
5) when not in use, removed from working area

## Slide 13: GEARBOX RIGGING

## Slide 14: Rigging Considerations
POSITIVE CONNECTION
ROTATION
EQUALIZATION
CENTER OF GRAVITY

## Slide 15: Rigging Equipment Slings
Types of slings covered are those made from alloy steel chain, wire rope, metal mesh, natural or synthetic fiber rope, and synthetic web.
Chain
Wire rope
Metal mesh
Synthetic

## Slide 16
Adapts to shape of the load
Can be damage by sudden shocks
Best choice for hoisting very hot materials
Must have an affixed tag stating size, grade, rated capacity, and sling manufacturer
Alloy Steel Chains

## Slide 17
Alloy Steel Chain Attachments
Rated Capacity
Hooks, rings, oblong links, or other attachments, when used with alloy steel chains, must have a rated capacity at least equal to that of the chain

## Slide 18
Unsuitable Alloy Steel Chain Attachments
  Job or shop hooks and links, or makeshift fasteners, formed from bolts, rods, etc., or other altered attachments, can’t be used
Right
Wrong

## Slide 19: Wire Rope Slings
Used to hoist materials
Selection considerations:
  strength
  ability to bend without cracking
  ability to withstand abrasive wear
  ability to withstand abuse
Wire rope
Strand
Center
Wire
Core

## Slide 20
Wire Rope Slings Cont.
If these happen, remove the wire rope sling from service
Crushing
Kinking
Bird Caging

## Slide 21
Wire Rope Clips
When using U-bolt wire rope clips to form eyes, ensure the "U" section is in contact with the dead end of the rope
This is the correct method

## Slide 22: Synthetic Web Sling Markings
Mark or code to show:
  Name or trademark of manufacturer
  Rated capacities for the type of hitch
  Type of material

## Slide 23: Synthetic Web Slings Fittings
Fittings must be:
  At least as strong as that of the sling
  Free of sharp edges that could damage the webbing

## Slide 24: Synthetic Web Slings - Remove from Service
Remove from service if any of these are present:
  Acid or caustic burns
  Melting or charring of any part
  Snags, punctures, tears or cuts
  Broken or worn stitches
  Distortion of fittings
Heat Damage

## Slide 25: Lifting and Moving
Make sure hands are clear of potential pinch points
No one is positioned between load and another object
Slowly raise hoist block to remove slack
Slings are fully seated
Lift load a few inches to check rigging
Lift load high enough to clear obstructions.

## Slide 26: Don’ts
Jog controls unnecessarily
Use pendant control station to swing jib boom into place
Leave suspended load unattended
Pass load over people or allow anyone to walk under it.
Pull a load
Get distracted
Allow unused slings or ropes to remain on the hook
Leave hoist block low enough to hit someone.

## Slide 27: BASIC HITCHES Load Angle Factor
1000 lbs.
1000 lbs.
1000 lbs.
1000 lbs.
60 degree angle
10 degree
angle
30 degree angle
45 degree angle
577 lbs.
707 lbs.
1000 lbs.
2874 lbs.
L
H

## Slide 28: Calculation vs LAF Table
Sling Angle | LAF
90 | 1.000
60 | 1.155
45 | 1.414
30 | 2.000
20 | 2.924
10 | 5.747
5 | 11.49
L/H = LAF
LAF X Load weight = Total Stress
Total Stress x Load Weight Distribution = Stress Per Leg
Danger

## Slide 29: Signalperson
Signalperson must be qualified by 3rd party or employer qualified evaluator
Qualification requirements are:
- know and understand the types of signals used and be competent in their use
- have basic understanding of equipment operation and limitations
- demonstrate they meet above requirements through written and oral test

## Slide 30: Signalperson
When signalperson is needed:
- the load travel / placement area is not in full view
- the view in the direction of travel is obstructed
- either operator or load handler determines it is necessary

## Slide 32: EXAM QUESTION # 1
Under the new crane standard, you must be certified by an accredited program before you are able to use a crane? (Here at CURI)
a) Absolutely
b) Designated operators can operate cranes in industrial operations
c) Experience and past knowledge will exempt the requirement
d) Certification cards can be purchased online to show certification

## Slide 33: EXAM QUESTION # 1
Under the new crane standard, you must be certified by an accredited program before you are able to use a crane? (Here at CURI)
a) Absolutely
b) Designated operators can operate cranes in industrial operations
c) Experience and past knowledge will exempt the requirement
d) Certification cards can be purchased online to show certification

## Slide 34: EXAM QUESTION # 2
Rigging equipment must be inspected how often?
a) Prior to each shift
b) Once Daily
c) prior to use on each shift and as necessary during the use to ensure that it is safe
d) Before quitting time

## Slide 35: EXAM QUESTION # 2
Rigging equipment must be inspected how often?
a) Prior to each shift
b) Once Daily
c) prior to use on each shift and as necessary during the use to ensure that it is safe
d) Before quitting time

## Slide 36: EXAM QUESTION # 3
Who must perform inspections on slings?
a) Anyone with knowledge and training
b) Only trained supervisors
c) A competent person
d) Only iron workers

## Slide 37: EXAM QUESTION # 3
Who must perform inspections on slings?
a) Anyone with knowledge and training
b) Only trained supervisors
c) A competent person
d) Only iron workers

## Slide 38: EXAM QUESTION # 4
When using U-bolt wire rope clips to form eyes, ensure the "U" section is in contact with the __________ of the rope?
a) Live end
b) Dead end
c) Both ends
d) No ends

## Slide 39: EXAM QUESTION # 4
When using U-bolt wire rope clips to form eyes, ensure the "U" section is in contact with the __________ of the rope?
a) Live end
b) Dead end
c) Both ends
d) No ends

## Slide 40: EXAM QUESTION # 5
Operators using cranes, derricks and chain falls < 1 ton need not to be trained in the proper operation and hazards?
a) True
b) False

## Slide 41: EXAM QUESTION # 5
Operators using cranes, derricks and chain falls < 1 ton need not to be trained in the proper operation and hazards?
a) True
b) False

## Slide 42: EXAM QUESTION # 6
A signalperson is needed when the load placement location is obstructed or not in full view?
a) True
b) False

## Slide 43: EXAM QUESTION # 6
A signalperson is needed when the load placement location is obstructed or not in full view?
a) True
b) False

## Slide 44: QUESTIONS?